## Slide 1: End-of-Year Project
Smart Locker System
2nd year in Electronics and Communications Engineering
Academic year : 2022 - 2023
Elaborated by :
Maghrebi Mohamed Ali
Ben Romdhane Melek
Supervisor :
Mr. Fakhfakh Mourad
Department of Electronics and Communications
Notes: Good morning; we are maghrebi mohamed ali and ben romdhane melek ;
Wen are glad to present to you our end of year project named smart locker system supervised by Mr Mourad fakhfakh

## Slide 2: 01. Introduction 02. Proposed solution 03. Hardware design 04. Software design 05. Conclusion 06. Perspectives
Plan
Notes: Our plan consists of six parts first ,,,,,,,,,, second ,,,,,,,,,,,, third ,,,,,,,,,,,, forth ,,,,,,,,,,,,,, we conclude by conclusion and perspective

## Slide 3: Review of the EXISTING infrastructure
Electric magnetic lock
Traditional locking mechanisms refer to physical locks that have been used for centuries to secure personal valuables.
Padlocks
Electronic locking systems are a type of locking mechanism that use electronic components to control access to a locked object.
They provided a basic level of protection.
Notes: Our project present a solution for an existing infrastructure which are ,,,,,,,,,,,,,,,,,,,,,

## Slide 4
Problematic situation
How can the transition from traditional electric locks and padlocks to an intelligent solution based on SMART technologies enhance the efficiency and security of locking systems?
What steps are required to implement this transition, and what is the impact on operational efficiency and associated costs?
Notes: So ,,,,,,,,,,,,,,, and

## Slide 5: Introduction 01

## Slide 6: Overview of Smart electronic locking systems
Smart Electronic locking systems are a type of locking mechanism that use electronic and biometric components to control access to a locked object
They are designed to provide enhanced security, access control compared to traditional locking mechanisms.
1

## Slide 7: Proposed Solution 02

## Slide 8: Solution
Short teComponents
Long Goals
The Smart Locker System solution is comprised of three main components: facial recognition, QR code, and RFID tag.
By using a combination of facial recognition, QR code, and RFID tag technologies, the proposed Smart Locker System solution provides a range of options for users to access lockers quickly and easily
2

## Slide 9: Use cases
Public places
01
Work places
02
Banks
03
The Smart Locker System solution offers a wide range of use cases and can be applied in various settings where secure and convenient storage is needed
3

## Slide 10: Solution modeling
The sequence diagram
The state machine diagram
It provides a detailed view of the different states of the system and the transitions between them, it is used to show how the system behaves
The use case diagram
4

## Slide 11
We will give more attention to the State machine diagram
State machine diagram
5

## Slide 12: 03 Hardware Design and Implementation
Notes: We move now to the section of hardware

## Slide 13: Hardware components
NodeMCU ESP-8266
The Smart Locker System is comprised of several hardware components, each playing a crucial role in the system's functioning. In this section, we will discuss each component in detail, including its physical and technical specifications.
The next table presents a comparison between the NodeMCU and the different boards:
Board | Wifi capability | Digital I/O Pins | Analog I/O Pins | Frequency | Other characteristics
NodeMcu ESP 8266 | Built in Module Wifi | 11 | 1 | 80MHZ | Suitable for low-power applications
STM32F407VGT6 | Wifi module required | 82 | 16 | 1.4GHZ to 1.5GHZ | Suitable for embedded systems and microcontroller-based projects
Raspberry-Pi 3 | Built in Module Wifi | 17 | No one | 72 MHZ to 120 MHZ | Full-fledged computer with rich features and capabilities
Arduino uno | Wifi module required | 14 | 6 | 16 MHZ to 48 MHZ | Popular platform for prototyping and DIY projects
6
Notes: We start with NodeMcu board ,,, this frequency is ranged between ,,,,,, and ,,,,,,,,,,,,,,,,, for STM32 module wi need an external wifi module

## Slide 14
ESP32-CAM module
TTL to USB module
OLED display module
Kit RFID RC522 Reader
Other components
7
Notes: Also we have an ESPCam module for face recognition and Qr detection, the ttl to usb module to upload script in the ESP cam ; the Oled to diplay information ; moreover the Kit RFID for the identifation and finally we have other component like batteries breadboars wires lesd with resistors

## Slide 15: Hardware integration, Design and implementation
The system utilizes the UART and I2C interfaces for communication. These interfaces enable efficient data exchange between the NodeMCU8266 board and the different components.
To create these connections, we used a software tool called Fritzing
8
Notes: The module esp is cabled with TTL to usb ; the powe on of board which are connected with OLED via SCL, SDA ,GND and Vcc ; thes ome choice for RC522 ; also we need two leds with resistors to shows the final informations of systems
SCL : Serial Clock SDA : Serial Data

## Slide 16: Software Design 04

## Slide 17: Technologies
The Smart Locker System is made up of several software components
We used the following tools to accomplish the project
Arduino IDE
VS code
XAMPP
Used to program the NODEMCU ESP8266 microcontroller, which controls the system's hardware components
This is an integrated development environment (IDE) used to write the software code that runs on the Smart Locker System
This is a cross-platform web server solution used to manage the Smart Locker System. It includes the Apache web server, MySQL database, and PHP interpreter
9

## Slide 18: Technologies
The Smart Locker System is made up of several software codes and libraries
Arduino IDE
Python codes
HTML codes
Codes:
Esp.ino: sets up a web server that allows users to control the ESP32 camera module.
Nodemcu.ino: An Arduino script for an RFID tag, OLED display and Led command
Codes:
QRgen.py : generate QR codes from a given string and save them as PNG files
esp.py : sets up a TCP/IP socket server between Mysql and ESP8266
Face.py: The program captures an image, detects faces, and compares them with MySQL data base.
QR.py: read QR codes from a live video stream and mark attendance in a database.
Codes:
Information.html:displays a table of client information with five columns
Sys.html: provides a table of hardware and software requirements
Home.html: describes the main content of work by linking to external resources
10

## Slide 19: Technologies
The Smart Locker System is made up of several software codes and libraries
PHP codes
Libraries
Codes:
Index.php: uses HTML, CSS, JavaScript, and PHP to display attendance records in a table format and includes a live video feed from an ESP-32 CAM. .
MFRC522 library : to interface with the RFID reader
Adafruit SSD1306 library: to display the tag ID on an OLED display
RFID Scan & Display
OpenCV, face_recognition, and MySQL: code Face .py
OpenCV, Pyzbar and MySQL: code QR .py
Face Recognition
QR Scan
11

## Slide 20
Arduino IDE
XAMPP
VS code
OLED.ino
TEST
TEST
Final_Script.ino
Apache
MySQL
Autorun.py
Face.py
QR.py
ESP.py
01
02
03
ESP Cam
ESP Cam
RFID Scanner
Data base
Data base
Data base
QR gen
FLASK
Informations Page
Browser
Home.html
Style.css
Index.css
Port 17
Port 17
Port 17
Port 3306
Port 3306
Port 3306
Port 80
Port 80
Port 80
Port 5002
Port 80 +3306
ESP.ino
IP CAM
RFID.ino
01
To facilitate the connection between the software architecture, a schematic can be used as a visual representation of the system components and their relations
Software components relations
12
Notes: Which create

## Slide 21
13

## Slide 22: Energy Consumption Analysis
DC power supply | 3800 mA/H
RFID Reader | 16 mA
Oled Display | 15 mA
LED indicators with 220 Ohm resistors | 5,9 mA
ESP-32 Cam | 180 mA
ESP8266 Board | 72 mA
Duration of power supply =
26 Hour and 18 Minute
1 DAY ; 2 Hours ; 18 Minute
14

## Slide 23
Economic study
The total cost of the project, based on the components used, is 198.500 TND
ESP8266 Nodemcu - 30.000 TND
ESP-32 cam - 60.000 TND
OLED display - 23.500 TND
RFID RC-522 and tags - 25.000 TND
TTL to USB module - 10.000 TND
Two power energy 12 V with support - 35.000 TND
Two breadboards - 10.000 TND
Other components like wires, LED, and resistors - 5.000 TND
This cost includes the following hardware components and their respective prices:
15

## Slide 24
Project Timeline
The project was realized over a period of two months:
One month dedicated to documentation
Another month allocated for the actual work
16

## Slide 25
The implementation of the system has been discussed in details, including the hardware components, the software tools with different programming languages and libraries
The Smart Locker System presented is an innovative solution that offers high-security storage facilities with the latest technologies, such as AI and IoT
Conclusion
17

## Slide 26
The Smart Locker System offers a promising perspective for the future. By integrating with existing infrastructure and incorporating a door actuator solution
Perspectives
We can incorporate a feature that includes an alarm or an SMS alert that will be triggered when the number of false entrance conditions exceeds three consecutive repetitions
We have established three conditions to enhance the system and explore additional technologies However, the client has the freedom to choose the options that best suit their own system preferences
18